**************DRAFT**************
SDRAM
11/01/18
**************DRAFT**************

For the ICOBoard you did not use PLL due hardware issues(PLL & SRAM) would a PLL be best for the catzip & sdram? Looking at the DCM lines 116 to 122 of xulalx25soc?
Starting looking at how the xulalx25soc intergrates the sdram.

Using autofpga to add sdram & sdramscope support to catzip
Both the xula2-lx25 & xula2-lx9 & catzip use the same sdram IC.
The xulalx25soc runs on the xula2-lx25 & xula2-lx9 and the has a verilator
simulation. The xulalx25soc design has a sdram C++ simulator implemented in
the files sdramsim.cpp & sdramsim.h. In addition the xulalx25soc design
has the wbsdram.v file which currently builds the toplevel.bit for
the xula2-lx9 or xula2-lx25.

Create the sdramdev.txt file to be used by autodata to include
in the toplevel.v & main.v which is instaniated by toplevel.v

This is what goes in toplevel.v
module toplevel(i_clk,
        i_ram_feedback_clk, o_ram_clk, o_ram_cke, o_ram_cs_n, o_ram_ras_n, o_ram_cas_n,
        o_ram_we_n, o_ram_bs, o_ram_addr, o_ram_udqm, o_ram_ldqm,
        io_ram_data,

        //o_ram_cs_n, Chip select
        //o_ram_cke, Clock enable
        //o_ram_ras_n, Row address strobe
        //o_ram_cas_n, Column address strobe
        //o_ram_we_n, Write enable
        //o_ram_bs, Bank select
        //o_ram_addr, Address lines
        //r_ram_data, Data lines (input)
        //ram_data, Data lines (output)
        input i_ram_feedback_clk;
        output wire o_ram_clk, o_ram_cke;
        output wire o_ram_cs_n, o_ram_ras_n, o_ram_cas_n, o_ram_we_n;
        output wire [1:0] o_ram_bs;
        output wire [12:0] o_ram_addr;
        output wire o_ram_udqm, o_ram_ldqm;
        inout wire [15:0] io_ram_data;
        wire [15:0] ram_data;
        wire ram_drive_data;
        //wire o_ram_drive_data;
        reg [15:0] r_ram_data;

        reg [1:0] o_ram_dqm;
        //using instead { o_ram_udqm, o_ram_ldqm }
        wire [31:0] o_debug;
.
.
.
       main thedesign(s_clk, s_reset,
        //*********************************************************
        //This section was missing when the simulation was aborting
        //xulalx25soc/rtl/busmaster.v same as main.v in new design
        //o_ram_cs_n, o_ram_cke, o_ram_ras_n, o_ram_cas_n,
        //o_ram_we_n, o_ram_bs, o_ram_addr,
        //o_ram_drive_data, i_ram_data, o_ram_data,
        //o_ram_dqm,
        //o_ram_drive seems to be the same as ram_drive_data
        //o_ram_drive_data was added to SIM.TICK and the assert(driv);
        //sdramsim.cpp restored write
        //assert(!driv); sdramsim.cpp restored read
        //*********************************************************

        o_ram_cs_n, o_ram_cke, o_ram_ras_n, o_ram_cas_n, o_ram_we_n,
        o_ram_bs, o_ram_addr,
        ram_drive_data, i_ram_data, o_ram_data, { o_ram_udqm, o_ram_ldqm },
        o_debug
    ,
        // GPIO wires
.
.
.
      // SDRAM Interface
        //
        // Use the PPIO primitive to give us access to a group of SB_IO's,
        // and therefore access to a tristate output
        //
        ppio #(.W(16))
        sdramioi(o_ram_we_n, io_ram_data, o_ram_data, i_ram_data);
assign o_ram_clk = clk_50mhz;
This is what goes in main.v
`ifdef SDRAM_ACCESS
wbsdram sdrami(i_clk,
        wb_cyc, (wb_stb)&&(sdram_sel),
        /* verilator lint_off WIDTH */
        wb_we, wb_addr[(25-3):0], wb_data, wb_sel,
        /* verilator lint_off WIDTH */
        sdram_ack, sdram_stall, sdram_data,
        o_ram_cs_n, o_ram_cke, o_ram_ras_n, o_ram_cas_n, o_ram_we_n,
        o_ram_bs, o_ram_addr,
        ram_drive_data, i_ram_data, o_ram_data, o_ram_dqm,
        o_debug);

`else // SDRAM_ACCESS

        // In the case that there is no sdram peripheral responding on the wb bus
        reg r_sdram_ack;
        initial r_sdram_ack = 1'b0;
        always @(posedge i_clk) r_sdram_ack <= (wb_stb)&&(sdram_sel);
        assign sdram_ack = r_sdram_ack;
        assign sdram_stall = 0;
        assign sdram_data = 0;

`endif // SDRAM_ACCESS

Adding a scope to debug the sdram issue
Create the sdramscope.txt file to be used by autodata to include
in the main.v which is called by toplevel.v

This is what goes in main.v
        assign sdram_debug = { (!o_ram_ce_n),
        wb_cyc, (wb_stb)&&(sdram_sel), wb_we,
        sdram_stall,sdram_ack,
        o_ram_ce_n, o_ram_oe_n, o_ram_we_n, o_ram_sel,
        o_ram_addr[4:0],
        (!o_ram_oe_n) ? i_ram_data[15:0]
        : o_ram_data[15:0]
        };
        wbscope #(.LGMEM(4), .SYNCHRONOUS(1), .HOLDOFFBITS(4))
        sdramscopei(i_clk, 1'b1, (!o_ram_ce_n), sdram_debug,
        i_clk, wb_cyc, (wb_stb)&&(sdramscope_sel),
        wb_we, wb_addr[0], wb_data,
        sdramscope_ack, sdramscope_stall, sdramscope_data,
        sdramscope_int);

This is what get added to design.h
18,20d17
< #define	SDRAM_SCOPE
< #endif
< #ifdef	SDRAM_ACCESS
45,47d41
< #ifdef	SDRAM_SCOPE
< #else	// SDRAM_SCOPE
< #endif	// SDRAM_SCOPE

Trying to add sdram support to the catzip. Steps
The command “python main_sdramdev.py”
creates sdramdev.v & Sdcntl.v Verilog files and the testbench main_sdramdev_tb.vcd.
Steps to obtain the Values Change Dump VCD. This creates the files sdramdev.v & Sdcntl.v
Modified the /testbuilds/catzip_simulated/catzip/sim/verilated/Makefile
to add the sdramsim.cpp to /testbuilds/catzip_simulated/catzip/sim/verilated/arm-main_tb.
The disassemble is found at
Appendix D: Disassemble of testbuilds/catzip_simulation/catzip/sim/verilated/arm-main_tb where the SDRAMSIM

Note:	Only one sdramdev_inst.convert(name = 'sdramdev') or SdCntl_inst.convert(name = 'Sdcntl')
can be uncommeted at the same time
 not both or the following error will occur
 Signal has multiple drivers: host_intf_rst_i

In the directory /home/pi/testbuilds/learning_hdl/MyHDL/sdram
“rm -f *.vcd”
“python main_sdramdev.py”
“gtkwave main_sdramdev_tb.vcd”
Create sdramdev.txt this is currently a draft version for use with	/home/pi/testbuilds/catzip_simulated/catzip/auto-data for the catzip.
 /home/pi/testbuilds/catzip_simulated/catzip/auto-data for the catzip.
/home/pi/testbuilds/catzip_simulated/catzip/make autodata
Copying auto-data/toplevel.v to rtl/catzip/toplevel.v
Copying auto-data/main.v to rtl/catzip/main.v
Copying auto-data/regdefs.h to sw/host/regdefs.h
Copying auto-data/regdefs.cpp to sw/host/regdefs.cpp
Copying auto-data/board.h to sw/board/board.h
Copying auto-data/board.ld to sw/board/board.ld
Copying auto-data/rtl.make.inc to rtl/catzip/auto.mk
Copying auto-data/main_tb.cpp to sim/verilated/main_tb.cpp
Copying auto-data/testb.h to sim/verilated/testb.h
Steps to obtain the Values Change Dump VCD. This creates the file sdramdev.v.

Add the sdramsim.cpp & sdramsim.h to /testbuilds/catzip_simulated/catzip/sim/verilated.

Steps used to get a working catzip
“cd catzip”
“. ./myenv.sh”
“make datestamp”
“make autodata”
“cd rtl/catzip”
“make” This command creates catzip.bin that can downloaded to FPGA. The Yosys Tools
were used.
“cd ../../sim/verilated”
“make” This command creates arm-main_tb used to simulate the HX8K FPGA
“cd ../../sw/host” This creates
”make” This command creates arm-netpport & arm-wbregs

The script restores “config_catzip_simulation.sh” located in the learning_hdl/MyHDL/sdram folder.
Starts with a working catzip
1st shell
. /home/pi/testbuilds/catzip_simulation/catzip/myenv.sh
/home/pi/testbuilds/catzip_simulation/catzip/
make autodata
2nd shell
. /home/pi/testbuilds/catzip_simulation/catzip/myenv.sh
/home/pi/testbuilds/catzip_simulation/catzip/rtl/catzip
make clean
make cpudefs.h
make design.h
make verilated
make bin
/home/pi/testbuilds/catzip_simulation/catzip/sim/verilated/
make clean
make
3rd shell
. /home/pi/testbuilds/catzip_simulation/catzip/myenv.sh
cd testbuilds/catzip_simulation/catzip/sim/verilated/
make clean
make
./arm-main_tb
The script used to execute the arm-wbregs command is found at Appendix A: Script that executes the arm-wbregs commands sim_hw_test.sh
The output of the arm-main_tb is found at Appendix B: CATZIP testing the verilator simulation.
Listening on port 8363
Listening on port 8364
> T
In 4th shell
. /home/pi/testbuilds/catzip_simulation/catzip/myenv.sh
cd testbuilds/catzip_simulation/catzip/sw/host/
./sim_hw_test.sh
The output of the sim_hw_test.sh is found at Appendix C: CATZIP testing the verilator simulation running wbregs command from the script
sim_hw_test.sh .
cp testbuilds/learning_hdl/MyHDL/sdram/ topsdcntl.v & SdramCntl.v ~/testbuilds/catzip_simulation/catzip/rtl/catzip/
cp ~/testbuilds/learning_hdl/MyHDL/sdram/sdramdev.txt ~/testbuilds/catzip_simulation/catzip/auto-data/
cp ~/testbuilds/learning_hdl/MyHDL/sdram/Makefile_autodata ~/testbuilds/catzip_simulation/catzip/auto-data/Makefile
Note This provides a verilator sim of both sram & blkram
. ~/testbuilds/catzip_simulation/catzip/myenv.sh
cd ~/testbuilds/catzip_simulation/catzip/autodata

Create sdcntl.txt
Modified Makefile in ~/testbuilds/catzip_simulation/catzip/autodata → Makefile_autodata

The Catboard has HX8K FPGA with a SDRAM that provides 0x000000 to 0xFFFFFF 16 bit locations.
The SDCONTROLLER takes care of refreshing the SDRAM and interface between the FPGA and the SDRAM. The data 0x05DC 1500 is being wrote to address 0x000BB8 3000, the data 0xFFFF 65535 is being wrote to address 0xFFFFFF 16777215. Then the data is read from
address 0x000BB8 3000.

This test writes two SDRAM address and reads the value wrote to first location.
The data 0x05DC 1500 is being wrote to address 0x00000BB8 3000, 0xFFFF 65535 is being wrote to address 0x00FFFFFF 16777215. This is followed by reading the value at
address 0x00000BB8 3000 which was 0x05DC 1500.

BANK 0 STATE : [CHANGE] Uninitialized -> Initialized @ 2138
 BANK 1 STATE : [CHANGE] Uninitialized -> Initialized @ 2138
 BANK 2 STATE : [CHANGE] Uninitialized -> Initialized @ 2138
 BANK 3 STATE : [CHANGE] Uninitialized -> Initialized @ 2138
--------------------------
 Mode | CAS | Burst
--------|-------|---------
 Burst | 3 | 1
--------------------------
 SDRAM : Bank 0 has active row 0005
 BANK 0 STATE : WRITING @ 2514
 DATA : [WRITE] Addr: 440 Data: 1500
The data 0x05DC 1500 is being wrote to address 0x000BB8 3000 Row 0005 col Addr: 440 0x1B8 is where the 1500 0x05DC is written.

SDRAM : Bank 3 has active row 1fff
 BANK 3 STATE : WRITING @ 2652
 DATA : [WRITE] Addr: 511 Data: 65535
 BANK 3 STATE : WRITING TO 01ff:511

The data 0xFFFF 65535 is being wrote to address 0xFFFFFF 16777215 (this is the last location in the sdram) Row 1FFF col Addr: 511 0x1FF is where the 65535 0xFFFF is written.

SDRAM : Bank 0 has active row 0005
 BANK 0 STATE : READING @ 2790
 SDRAM : [READ] Commnad registered
 BANK 0 STATE : READING FROM 01b8:440
 STATE : [READ] Data Ready @ 2794 value : 1500

 BANK 0 STATE : WRITING TO 01b8:440
4400440: 1500
 SDRAM : Bank 3 has active row 1fff
 BANK 3 STATE : WRITING @ 2652
 DATA : [WRITE] Addr: 511 Data: 65535
 BANK 3 STATE : WRITING TO 01ff:511
4400440: 1500
5110511: 65535
 SDRAM : Bank 0 has active row 0005
 BANK 0 STATE : READING @ 2790
 SDRAM : [READ] Commnad registered
 BANK 0 STATE : READING FROM 01b8:440
 STATE : [READ] Data Ready @ 2794 value : 1500

In the image below the data 0x05DC 1500 is being wrote to address 0x00000BB8 3000, 0xFFFF 65535 is being wrote to address 0x00FFFFFF 16777215. This is followed by reading the value at
address 0x00000BB8 3000 which was 0x05DC 1500.
BANK 3 STATE : WRITING @ 2652

 DATA : [WRITE] Addr: 511 Data: 65535
 BANK 3 STATE : WRITING TO 01ff:511

SDRAM : Bank 0 has active row 0005
 BANK 0 STATE : WRITING @ 2514
 DATA : [WRITE] Addr: 440 Data: 1500
 BANK 0 STATE : WRITING TO 01b8:440
In the image below the data 0x05DC 1500 is being wrote to address 0x000BB8 3000

SDRAM : Bank 3 has active row 1fff
 BANK 3 STATE : WRITING @ 2652
 DATA : [WRITE] Addr: 511 Data: 65535
 BANK 3 STATE : WRITING TO 01ff:511
In the image below the data 0xFFFF 65535 is being wrote to address 0xFFFFFF 16777215.

BANK 0 STATE : READING @ 2790
 SDRAM : [READ] Commnad registered
 BANK 0 STATE : READING FROM 01b8:440
 STATE : [READ] Data Ready @ 2794 value : 1500
In the image below reading the value at address 0x00000BB8 3000 which was 0x05DC 1500.

The memory_test takes approximately 3.5 sec or 175e6 clocks to complete at 50MHz. The memory_test writes to 16777215 locations and reads the data written.

Catboard running top.bin after the program has been load starting to write to memory during the memory_test

Catboard running top.bin after the program has been load starting to read from memory during the memory_test

Catboard running top.bin after the program has been load and the end memory memory_test. Note all 4 leds are on.

Now the sdram_test is memdev
module top (
    clk100MHz,
    sdram_clk,
    sdram_return_clk,
    led_status,
    pb,
    memdev0_SdramCntl0_sd_intf_cke,
    memdev0_SdramCntl0_sd_intf_we,
    memdev0_SdramCntl0_sd_intf_addr,
    memdev0_SdramCntl0_sd_intf_dqml,
    memdev0_SdramCntl0_sd_intf_cas,
    memdev0_SdramCntl0_sd_intf_dqmh,
    memdev0_SdramCntl0_sd_intf_ras,
    memdev0_SdramCntl0_sd_intf_bs,
    memdev0_SdramCntl0_sd_intf_cs,
    memdev0_SdramCntl0_sd_intf_dq
);
=== top ===

   Number of wires: 441
   Number of wire bits: 968
   Number of public wires: 84
   Number of public wire bits: 537
   Number of memories: 0
   Number of memory bits: 0
   Number of processes: 0
   Number of cells: 719
     $_TBUF_ 16
     SB_CARRY 68
     SB_DFF 4
     SB_DFFE 4
     SB_DFFER 98
     SB_DFFES 1
     SB_DFFESR 45
     SB_DFFESS 4
     SB_DFFR 52
     SB_DFFS 8
     SB_DFFSR 3
     SB_DFFSS 4
     SB_LUT4 412

Host interface signals
wire [23:0] memdev0_SdramCntl0_host_intf_addr_i;
wire [15:0] memdev0_SdramCntl0_host_intf_data_i;
wire [15:0] memdev0_SdramCntl0_host_intf_data_i;
wire [15:0] memdev0_SdramCntl0_host_intf_data_o;
wire memdev0_SdramCntl0_host_intf_done_o;
wire memdev0_SdramCntl0_host_intf_wr_i;
wire memdev0_memory_test0_host_intf_rst_i;

Write function
during a write
4 clks in between address chg
4 clks in between data chg
80 nsec
The 24 bit memdev0_SdramCntl0_host_intf_addr_i is set on the raising edge of clk. One clk later the 16 bit
memdev0_SdramCntl0_host_intf_data_i and memdev0_SdramCntl0_host_intf_wr_i goes hi. A clk later the memdev0_SdramCntl0_host_intf_done_o goes hi and the memdev0_SdramCntl0_host_intf_wr_i goes lo.

Read function

The 24 bit memdev0_SdramCntl0_host_intf_addr_i is set on the raising edge of clk. One clk later the 16 bit memdev0_SdramCntl0_host_intf_rd_i goes hi. Five clk later the memdev0_SdramCntl0_host_intf_done_o goes hi, memdev0_SdramCntl0_host_intf_data_o is valid and the memdev0_SdramCntl0_host_intf_rd_i goes lo.

During the first part of the memory_test Write takes place.

python memdev.py

make
sudo config_cat top.bin

2^24	16777216	0x000000	0xFFFFFF	16Bits
@PREFIX=sdram
@DEVID=SDRAM
@$LGMEMSZ=24
@LGMEMSZ.FORMAT=%d
@$NADDR=(1<<(@$THIS.LGMEMSZ-2))
@$NBYTES=(1<<(@$THIS.LGMEMSZ))
@NBYTES.FORMAT=0x%08x
@ACCESS=@$(DEVID)_ACCESS
@SLAVE.TYPE=MEMORY
@SLAVE.BUS=wb
@LD.PERM=wx
#!/bin/bash

Appendix A: Script that executes the arm-wbregs commands sim_hw_test.sh

#!/bin/bash

echo "The date built"
./arm-wbregs version
sleep 2
./arm-wbregs 0x700 0x10000001
sleep 2
./arm-wbregs 0x704 0x10000002
sleep 2
./arm-wbregs 0x708 0x10000003
sleep 2
./arm-wbregs 0x70c 0x10000004
sleep 2
./arm-wbregs 0x700
sleep 2
./arm-wbregs 0x704
sleep 2
./arm-wbregs 0x708
sleep 2
./arm-wbregs 0x70c
sleep 2
echo "Turning on the 4th led "
./arm-wbregs gpio 0x00010001
sleep 2
echo "Turning on the 1st led "
./arm-wbregs gpio 0x00020002
sleep 2
echo "Turning on the 2nd led "
./arm-wbregs gpio 0x00040004
sleep 5
echo "Turning off the leds "
./arm-wbregs gpio 0x00070000

 Appendix B: CATZIP testing the verilator simulation.
./arm-main_tb
Listening on port 8363
Listening on port 8364
Accepted CMD connection
POLL = 1
RCVD: 6 bytes
< A611R
> A00000611R20180812
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 14 bytes
< A701W10000001
> A00000701
> K00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 14 bytes
< A705W10000002
> A00000705
> K00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 14 bytes
< A709W10000003
> A00000709
> K00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 14 bytes
< A70dW10000004
> A0000070d
> K00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 6 bytes
< A701R
> A00000701R10000001
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 6 bytes
< A705R
> A00000705R10000002
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 6 bytes
< A709R
> A00000709R10000003
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 6 bytes
< A70dR
> A0000070dR10000004
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 11 bytes
< A609W10001
> A00000609K00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 11 bytes
< A609W20002
> A00000609K00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 11 bytes
< A609W40004
> A00000609K00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 11 bytes
< A609W70000
> A00000609K00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
> Z
CMD: Only sent 0 bytes of 3
 ^C
Appendix C: CATZIP testing the verilator simulation running wbregs command from the script
sim_hw_test.sh .
The date built
00000610 ( VERSION) : [....] 20180812
00000700 ( RAM)-> 10000001
00000704 ( )-> 10000002
00000708 ( )-> 10000003
0000070c ( )-> 10000004
00000700 ( RAM) : [....] 10000001
00000704 ( ) : [....] 10000002
00000708 ( ) : [....] 10000003
0000070c ( ) : [....] 10000004
Turning on the 4th led
00000608 ( GPIO)-> 00010001
Turning on the 1st led
00000608 ( GPIO)-> 00020002
Turning on the 2nd led
00000608 ( GPIO)-> 00040004
Turning off the leds
00000608 ( GPIO)-> 00070000
Chgs after adding sdcntl.txt & sdramdev.txt blkram move from 0x700 to 0x00800000
The date built
00600010 ( VERSION) : [....] 20180812
00800000 ( RAM)-> 10000001
00800004 ( )-> 10000002
00800008 ( )-> 10000003
0080000c ( )-> 10000004
00800000 ( RAM) : [....] 10000001
00800004 ( ) : [....] 10000002
00800008 ( ) : [....] 10000003
0080000c ( ) : [....] 10000004
Turning on the 4th led
00600008 ( GPIO)-> 00010001
Turning on the 1st led
00600008 ( GPIO)-> 00020002
Turning on the 2nd led
00600008 ( GPIO)-> 00040004
Turning off the leds
00600008 ( GPIO)-> 00070000

Appendix D: Disassemble of testbuilds/catzip_simulation/catzip/sim/verilated/arm-main_tb where the SDRAMSIM
 00024654 <_ZN8SDRAMSIMclEiiiiiiijiss>:
   2466c:	1a000004	bne	24684 <_ZN8SDRAMSIMclEiiiiiiijiss+0x30>
   24678:	1a000002	bne	24688 <_ZN8SDRAMSIMclEiiiiiiijiss+0x34>
   24680:	ea00001e	b	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24698:	0a00001a	beq	24708 <_ZN8SDRAMSIMclEiiiiiiijiss+0xb4>
   246a4:	ca0000c3	bgt	249b8 <_ZN8SDRAMSIMclEiiiiiiijiss+0x364>
   246ac:	1a000034	bne	24784 <_ZN8SDRAMSIMclEiiiiiiijiss+0x130>
   246c4:	1a000038	bne	247ac <_ZN8SDRAMSIMclEiiiiiiijiss+0x158>
   246cc:	0a000031	beq	24798 <_ZN8SDRAMSIMclEiiiiiiijiss+0x144>
   246d8:	0a00002e	beq	24798 <_ZN8SDRAMSIMclEiiiiiiijiss+0x144>
   246e4:	0a00002b	beq	24798 <_ZN8SDRAMSIMclEiiiiiiijiss+0x144>
   24708:	e59f496c	ldr	r4, [pc, #2412]	; 2507c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa28>
   24718:	e59f0960	ldr	r0, [pc, #2400]	; 25080 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa2c>
   24724:	e59f1958	ldr	r1, [pc, #2392]	; 25084 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa30>
   24734:	e59f194c	ldr	r1, [pc, #2380]	; 25088 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa34>
   24744:	e59f1940	ldr	r1, [pc, #2368]	; 2508c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa38>
   24754:	e59f1934	ldr	r1, [pc, #2356]	; 25090 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa3c>
   24764:	e59f1928	ldr	r1, [pc, #2344]	; 25094 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa40>
   24770:	e59f3920	ldr	r3, [pc, #2336]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24778:	e59f191c	ldr	r1, [pc, #2332]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   2477c:	e59f091c	ldr	r0, [pc, #2332]	; 250a0 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4c>
   24784:	e59f390c	ldr	r3, [pc, #2316]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   2478c:	e59f1908	ldr	r1, [pc, #2312]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24790:	e59f090c	ldr	r0, [pc, #2316]	; 250a4 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa50>
   24798:	e59f38f8	ldr	r3, [pc, #2296]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   247a0:	e59f18f4	ldr	r1, [pc, #2292]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   247a4:	e59f08fc	ldr	r0, [pc, #2300]	; 250a8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa54>
   247b0:	0a000019	beq	2481c <_ZN8SDRAMSIMclEiiiiiiijiss+0x1c8>
   247b8:	0a000028	beq	24860 <_ZN8SDRAMSIMclEiiiiiiijiss+0x20c>
   247c0:	0a000042	beq	248d0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x27c>
   247c8:	0a000057	beq	2492c <_ZN8SDRAMSIMclEiiiiiiijiss+0x2d8>
   247d0:	1affffc8	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   247d8:	1a000071	bne	249a4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x350>
   247e0:	1a00006f	bne	249a4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x350>
   247ec:	1a00006c	bne	249a4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x350>
   247f8:	0a000069	beq	249a4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x350>
   24804:	1affffbb	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24818:	ea00005d	b	24994 <_ZN8SDRAMSIMclEiiiiiiijiss+0x340>
   24820:	1affffb4	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24828:	1affffb2	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24834:	0affffaf	beq	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24840:	1affffac	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   2485c:	eaffffa5	b	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24868:	1a000009	bne	24894 <_ZN8SDRAMSIMclEiiiiiiijiss+0x240>
   2487c:	aaffff9d	bge	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24884:	e59f1820	ldr	r1, [pc, #2080]	; 250ac <_ZN8SDRAMSIMclEiiiiiiijiss+0xa58>
   24890:	eafffff7	b	24874 <_ZN8SDRAMSIMclEiiiiiiijiss+0x220>
   24898:	1a000007	bne	248bc <_ZN8SDRAMSIMclEiiiiiiijiss+0x268>
   248a0:	1a000005	bne	248bc <_ZN8SDRAMSIMclEiiiiiiijiss+0x268>
   248ac:	1a000002	bne	248bc <_ZN8SDRAMSIMclEiiiiiiijiss+0x268>
   248b8:	1affff8e	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   248bc:	e59f37d4	ldr	r3, [pc, #2004]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   248c4:	e59f17d0	ldr	r1, [pc, #2000]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   248c8:	e59f07e0	ldr	r0, [pc, #2016]	; 250b0 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa5c>
   248d4:	1affff87	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   248dc:	1affff85	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   248e8:	1affff82	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   248f4:	1affff7f	bne	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24900:	1a000004	bne	24918 <_ZN8SDRAMSIMclEiiiiiiijiss+0x2c4>
   24914:	eaffff77	b	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24918:	e59f3778	ldr	r3, [pc, #1912]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24920:	e59f1774	ldr	r1, [pc, #1908]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24924:	e59f0788	ldr	r0, [pc, #1928]	; 250b4 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa60>
   24930:	0a000007	beq	24954 <_ZN8SDRAMSIMclEiiiiiiijiss+0x300>
   2493c:	1a000009	bne	24968 <_ZN8SDRAMSIMclEiiiiiiijiss+0x314>
   24950:	eaffff68	b	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24954:	e59f373c	ldr	r3, [pc, #1852]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   2495c:	e59f1738	ldr	r1, [pc, #1848]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24960:	e59f0750	ldr	r0, [pc, #1872]	; 250b8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa64>
   2496c:	0affff61	beq	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   24970:	e59f3720	ldr	r3, [pc, #1824]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24978:	e59f171c	ldr	r1, [pc, #1820]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   2497c:	e59f0738	ldr	r0, [pc, #1848]	; 250bc <_ZN8SDRAMSIMclEiiiiiiijiss+0xa68>
   24988:	e59f171c	ldr	r1, [pc, #1820]	; 250ac <_ZN8SDRAMSIMclEiiiiiiijiss+0xa58>
   2499c:	bafffff8	blt	24984 <_ZN8SDRAMSIMclEiiiiiiijiss+0x330>
   249a0:	eaffff54	b	246f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa4>
   249a4:	e59f36ec	ldr	r3, [pc, #1772]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   249ac:	e59f16e8	ldr	r1, [pc, #1768]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   249b0:	e59f0708	ldr	r0, [pc, #1800]	; 250c0 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa6c>
   249c4:	aa000005	bge	249e0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x38c>
   249dc:	eafffff6	b	249bc <_ZN8SDRAMSIMclEiiiiiiijiss+0x368>
   249e4:	ea000000	b	249ec <_ZN8SDRAMSIMclEiiiiiiijiss+0x398>
   249f0:	ca00001a	bgt	24a60 <_ZN8SDRAMSIMclEiiiiiiijiss+0x40c>
   24a2c:	0affffed	beq	249e8 <_ZN8SDRAMSIMclEiiiiiiijiss+0x394>
   24a48:	aaffffe6	bge	249e8 <_ZN8SDRAMSIMclEiiiiiiijiss+0x394>
   24a4c:	e59f3644	ldr	r3, [pc, #1604]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24a54:	e59f1640	ldr	r1, [pc, #1600]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24a58:	e59f0664	ldr	r0, [pc, #1636]	; 250c4 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa70>
   24a78:	0a000003	beq	24a8c <_ZN8SDRAMSIMclEiiiiiiijiss+0x438>
   24a88:	0a000048	beq	24bb0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x55c>
   24a94:	da000010	ble	24adc <_ZN8SDRAMSIMclEiiiiiiijiss+0x488>
   24aa0:	0a00000d	beq	24adc <_ZN8SDRAMSIMclEiiiiiiijiss+0x488>
   24ac8:	1a000040	bne	24bd0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x57c>
   24af4:	1a000040	bne	24bfc <_ZN8SDRAMSIMclEiiiiiiijiss+0x5a8>
   24b20:	1a000046	bne	24c40 <_ZN8SDRAMSIMclEiiiiiiijiss+0x5ec>
   24b28:	1a000044	bne	24c40 <_ZN8SDRAMSIMclEiiiiiiijiss+0x5ec>
   24b34:	1a000041	bne	24c40 <_ZN8SDRAMSIMclEiiiiiiijiss+0x5ec>
   24b40:	0a00003e	beq	24c40 <_ZN8SDRAMSIMclEiiiiiiijiss+0x5ec>
   24b4c:	e59f1558	ldr	r1, [pc, #1368]	; 250ac <_ZN8SDRAMSIMclEiiiiiiijiss+0xa58>
   24b74:	1a000022	bne	24c04 <_ZN8SDRAMSIMclEiiiiiiijiss+0x5b0>
   24b80:	1a000024	bne	24c18 <_ZN8SDRAMSIMclEiiiiiiijiss+0x5c4>
   24b8c:	1a000026	bne	24c2c <_ZN8SDRAMSIMclEiiiiiiijiss+0x5d8>
   24b98:	0afffed8	beq	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24b9c:	e59f34f4	ldr	r3, [pc, #1268]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24ba4:	e59f14f0	ldr	r1, [pc, #1264]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24ba8:	e59f0518	ldr	r0, [pc, #1304]	; 250c8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa74>
   24bb0:	e59f34c4	ldr	r3, [pc, #1220]	; 2507c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa28>
   24bc0:	e59f0504	ldr	r0, [pc, #1284]	; 250cc <_ZN8SDRAMSIMclEiiiiiiijiss+0xa78>
   24bd4:	0affffbd	beq	24ad0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x47c>
   24be8:	0affffb8	beq	24ad0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x47c>
   24bf8:	eaffffb4	b	24ad0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x47c>
   24c00:	eaffffc0	b	24b08 <_ZN8SDRAMSIMclEiiiiiiijiss+0x4b4>
   24c04:	e59f348c	ldr	r3, [pc, #1164]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24c0c:	e59f1488	ldr	r1, [pc, #1160]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24c10:	e59f04b8	ldr	r0, [pc, #1208]	; 250d0 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa7c>
   24c18:	e59f3478	ldr	r3, [pc, #1144]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24c20:	e59f1474	ldr	r1, [pc, #1140]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24c24:	e59f04a8	ldr	r0, [pc, #1192]	; 250d4 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa80>
   24c2c:	e59f3464	ldr	r3, [pc, #1124]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24c34:	e59f1460	ldr	r1, [pc, #1120]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24c38:	e59f0498	ldr	r0, [pc, #1176]	; 250d8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa84>
   24c44:	1a000025	bne	24ce0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x68c>
   24c4c:	1a000023	bne	24ce0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x68c>
   24c58:	0a000020	beq	24ce0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x68c>
   24c64:	1a00001d	bne	24ce0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x68c>
   24c70:	0a00000b	beq	24ca4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x650>
   24c7c:	cafffe9f	bgt	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24ca0:	eafffff3	b	24c74 <_ZN8SDRAMSIMclEiiiiiiijiss+0x620>
   24cac:	1a000006	bne	24ccc <_ZN8SDRAMSIMclEiiiiiiijiss+0x678>
   24cc8:	eafffe8c	b	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24ccc:	e59f33c4	ldr	r3, [pc, #964]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24cd4:	e59f13c0	ldr	r1, [pc, #960]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24cd8:	e59f03fc	ldr	r0, [pc, #1020]	; 250dc <_ZN8SDRAMSIMclEiiiiiiijiss+0xa88>
   24ce4:	1a000032	bne	24db4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x760>
   24cec:	1a000030	bne	24db4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x760>
   24cf8:	0a00002d	beq	24db4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x760>
   24d04:	0a00002a	beq	24db4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x760>
   24d10:	1a000016	bne	24d70 <_ZN8SDRAMSIMclEiiiiiiijiss+0x71c>
   24d28:	1a000019	bne	24d94 <_ZN8SDRAMSIMclEiiiiiiijiss+0x740>
   24d50:	e59f2388	ldr	r2, [pc, #904]	; 250e0 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa8c>
   24d6c:	eafffe63	b	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24d78:	e59f32fc	ldr	r3, [pc, #764]	; 2507c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa28>
   24d88:	e59f0354	ldr	r0, [pc, #852]	; 250e4 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa90>
   24d90:	eaffffe5	b	24d2c <_ZN8SDRAMSIMclEiiiiiiijiss+0x6d8>
   24d98:	e59f1348	ldr	r1, [pc, #840]	; 250e8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa94>
   24d9c:	e59f02d8	ldr	r0, [pc, #728]	; 2507c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa28>
   24db0:	eaffffdd	b	24d2c <_ZN8SDRAMSIMclEiiiiiiijiss+0x6d8>
   24db8:	1a00008a	bne	24fe8 <_ZN8SDRAMSIMclEiiiiiiijiss+0x994>
   24dc0:	0a000088	beq	24fe8 <_ZN8SDRAMSIMclEiiiiiiijiss+0x994>
   24dcc:	1a000085	bne	24fe8 <_ZN8SDRAMSIMclEiiiiiiijiss+0x994>
   24dd8:	1a00003c	bne	24ed0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x87c>
   24de4:	1a00002a	bne	24e94 <_ZN8SDRAMSIMclEiiiiiiijiss+0x840>
   24dfc:	0a000029	beq	24ea8 <_ZN8SDRAMSIMclEiiiiiiijiss+0x854>
   24e30:	0a000021	beq	24ebc <_ZN8SDRAMSIMclEiiiiiiijiss+0x868>
   24e60:	0afffe26	beq	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24e88:	e59f3250	ldr	r3, [pc, #592]	; 250e0 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa8c>
   24e90:	eafffe1a	b	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24e94:	e59f31fc	ldr	r3, [pc, #508]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24e9c:	e59f11f8	ldr	r1, [pc, #504]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24ea0:	e59f0234	ldr	r0, [pc, #564]	; 250dc <_ZN8SDRAMSIMclEiiiiiiijiss+0xa88>
   24ea8:	e59f31e8	ldr	r3, [pc, #488]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24eb0:	e59f11e4	ldr	r1, [pc, #484]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24eb4:	e59f0230	ldr	r0, [pc, #560]	; 250ec <_ZN8SDRAMSIMclEiiiiiiijiss+0xa98>
   24ebc:	e59f31d4	ldr	r3, [pc, #468]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24ec4:	e59f11d0	ldr	r1, [pc, #464]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24ec8:	e59f0220	ldr	r0, [pc, #544]	; 250f0 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa9c>
   24ed8:	1a000033	bne	24fac <_ZN8SDRAMSIMclEiiiiiiijiss+0x958>
   24ef0:	0a000032	beq	24fc0 <_ZN8SDRAMSIMclEiiiiiiijiss+0x96c>
   24f04:	e59f21e8	ldr	r2, [pc, #488]	; 250f4 <_ZN8SDRAMSIMclEiiiiiiijiss+0xaa0>
   24f28:	1a000029	bne	24fd4 <_ZN8SDRAMSIMclEiiiiiiijiss+0x980>
   24f7c:	0afffddf	beq	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24fa0:	e59f3138	ldr	r3, [pc, #312]	; 250e0 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa8c>
   24fa8:	eafffdd4	b	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24fac:	e59f30e4	ldr	r3, [pc, #228]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24fb4:	e59f10e0	ldr	r1, [pc, #224]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24fb8:	e59f011c	ldr	r0, [pc, #284]	; 250dc <_ZN8SDRAMSIMclEiiiiiiijiss+0xa88>
   24fc0:	e59f30d0	ldr	r3, [pc, #208]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24fc8:	e59f10cc	ldr	r1, [pc, #204]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24fcc:	e59f0118	ldr	r0, [pc, #280]	; 250ec <_ZN8SDRAMSIMclEiiiiiiijiss+0xa98>
   24fd4:	e59f30bc	ldr	r3, [pc, #188]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   24fdc:	e59f10b8	ldr	r1, [pc, #184]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   24fe0:	e59f0110	ldr	r0, [pc, #272]	; 250f8 <_ZN8SDRAMSIMclEiiiiiiijiss+0xaa4>
   24fec:	1afffdc3	bne	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   24ff4:	0a000005	beq	25010 <_ZN8SDRAMSIMclEiiiiiiijiss+0x9bc>
   25000:	0a000002	beq	25010 <_ZN8SDRAMSIMclEiiiiiiijiss+0x9bc>
   2500c:	1afffdbb	bne	24700 <_ZN8SDRAMSIMclEiiiiiiijiss+0xac>
   25010:	e59f4064	ldr	r4, [pc, #100]	; 2507c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa28>
   25020:	e59f00d4	ldr	r0, [pc, #212]	; 250fc <_ZN8SDRAMSIMclEiiiiiiijiss+0xaa8>
   2502c:	e59f1054	ldr	r1, [pc, #84]	; 25088 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa34>
   2503c:	e59f1048	ldr	r1, [pc, #72]	; 2508c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa38>
   2504c:	e59f103c	ldr	r1, [pc, #60]	; 25090 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa3c>
   2505c:	e59f1030	ldr	r1, [pc, #48]	; 25094 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa40>
   25068:	e59f3028	ldr	r3, [pc, #40]	; 25098 <_ZN8SDRAMSIMclEiiiiiiijiss+0xa44>
   25070:	e59f1024	ldr	r1, [pc, #36]	; 2509c <_ZN8SDRAMSIMclEiiiiiiijiss+0xa48>
   25074:	e59f0084	ldr	r0, [pc, #132]	; 25100 <_ZN8SDRAMSIMclEiiiiiiijiss+0xaac>