Debugging Abort Issue
10/14/18
The simulation pc-main_tb Aborts when 9th
short	SDRAMSIM::operator()(int clk, int cke, int cs_n, int ras_n, int cas_n, int we_n,
int bs, unsigned addr, int driv, short data, short dqm)

parameter is sets to m_core→i_ram_data.
In the xulalx25soc the 9th parameter is set m_core→o_ram_drive_data.
The following is in toplevel of xulalx25soc design.
assign io_ram_data = (ram_drive_data) ? ram_data : 16'bzzzz_zzzz_zzzz_zzzz;
reg [15:0] r_ram_data_ext_clk;
// always @(posedge intermediate_clk_n)
always @(posedge clk_s)
r_ram_data_ext_clk <= io_ram_data;
always @(posedge clk_s)
r_ram_data <= r_ram_data_ext_clk;

When setting the 9th parameter to 21930 0x55aa the simulation does not Abort.
Setting the 9th parameter to o_ram_drive_data the simulation does not compile.

 @SIM.TICK=
#ifdef	@$(ACCESS)

m_core->i_ram_data = (*m_@$(MEM.NAME))(1,m_core->o_ram_cke,
m_core->o_ram_cs_n,m_core->o_ram_ras_n,m_core->o_ram_cas_n,
m_core->o_ram_we_n,m_core->o_ram_bs,m_core->o_ram_addr,
//m_core->o_ram_drive_data,m_core->o_ram_data,m_core->o_ram_dqm);
//21930,m_core->o_ram_data,m_core->o_ram_dqm);
m_core->i_ram_data,m_core->o_ram_data,m_core->o_ram_dqm);
#endif // @$(ACCESS)

./pc-wbregs 0x1000004 0x55aa
01000004 ( )-> 000055aa

./pc-main_tb
Listening on port 8363
Listening on port 8364
Successful settup! SDRAM switching to operational
Accepted CMD connection
POLL = 1
RCVD: 14 bytes
< A1000005W55aa
R/W Op
SDRAM[00000002] <= 0000
pc-main_tb: sdramsim.cpp:187: short int SDRAMSIM::operator()(int, int, int, int, int, int, int, unsigned int, int, short int, short int): Assertion `driv' failed.
Aborted (core dumped)

From toplevel.v xulalx25soc
assign io_ram_data = (ram_drive_data) ? ram_data : 16'bzzzz_zzzz_zzzz_zzzz;
reg [15:0] r_ram_data_ext_clk;
// always @(posedge intermediate_clk_n)
always @(posedge clk_s)
r_ram_data_ext_clk <= io_ram_data;
always @(posedge clk_s)
r_ram_data <= r_ram_data_ext_clk;

m_core->i_ram_data = m_sdram(1,
        m_core->o_ram_cke, m_core->o_ram_cs_n,
        m_core->o_ram_ras_n, m_core->o_ram_cas_n,
        m_core->o_ram_we_n, m_core->o_ram_bs,
        m_core->o_ram_addr, m_core->o_ram_drive_data,
        m_core->o_ram_data, m_core->o_ram_dqm);
0x55AA 21930

@SIM.TICK=
#ifdef	@$(ACCESS)

m_core->i_ram_data = (*m_@$(MEM.NAME))(1,m_core->o_ram_cke,
m_core->o_ram_cs_n,m_core->o_ram_ras_n,m_core->o_ram_cas_n,
m_core->o_ram_we_n,m_core->o_ram_bs,m_core->o_ram_addr,
21930,m_core->o_ram_data,m_core->o_ram_dqm);
//m_core->i_ram_data,m_core->o_ram_data,m_core->o_ram_dqm);
#endif // @$(ACCESS)

./pc-wbregs 0x1000004 0x55aa
01000004 ( )-> 000055aa

./pc-main_tb
Listening on port 8363
Listening on port 8364
Successful settup! SDRAM switching to operational
Accepted CMD connection
POLL = 1
RCVD: 14 bytes
< A1000005W55aa
R/W Op
SDRAM[00000002] <= 0000
SDRAM[00000002] <= 0000
SDRAM[00000003] <= 55aa
> A01000005K00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
Accepted CMD connection
POLL = 1
RCVD: 10 bytes
< A1000005R
R/W Op
SDRAM.Q[ 7] 55aa <= SDRAM[00000003]
> A01000005R00000000
POLL = 1
RCVD: 0 bytes
< [CLOSED]
^C