o_data[k] i_ram_data
 i_data[k] o_ram_data
io_data[k] io_ram_data
!i_dir o_ram_we_n

---
ppio #(.W(16))
sdramioi(o_ram_we_n, io_ram_data, o_ram_data, i_ram_data);
module	ppio(i_dir, io_data, i_data, o_data);
parameter	W=8;
input	i_dir;
inout	[(W-1):0]	io_data;
input	[(W-1):0]	i_data;
output	[(W-1):0]	o_data;
genvar	k;
generate
for(k=0; k<W; k = k+1)
SB_IO #(.PULLUP(1'b0),
.PIN_TYPE(6'b101001))
theio(
.OUTPUT_ENABLE(!i_dir),
.PACKAGE_PIN(io_data[k]),
.D_OUT_0(i_data[k]),
.D_IN_0( o_data[k])
);
endgenerate
endmodule

---
Write 0x2000000 0x55AAAA55
Address 0x0000 o_ram_data 0x55AA
o_ram_we_n & o_ram_cas_n & o_ram_dmod catzip
Error in simulation no lower 16 bits & hw
o_ram_data should be 0xaa55
Lower 16 bits get written to upper 16 bits hw

---
Address 0x0400 o_ram_data 0x55AA
o_ram_we_n & o_ram_ras_n
catzip
Error in simulation no lower 16 bits & hw
o_ram_data should be 0xaa55
Lower 16 bits get written to upper 16 bits hw

---
Address 0x0000 o_ram_data 0x55AA
o_ram_we_n & o_ram_cas_n & o_ram_dmod xulalx25soc

---
Address 0x0400 o_ram_data 0x55AA
o_ram_we_n & o_ram_ras_n
xulalx25soc
Error in simulation hw okay xulalx25soc
Should be o_ram_data 0xaa55