******************Draft******************
07/28/18
******************Draft******************

# Learning Hardware Description Language HDL
# For several years I have tried to learn Hardware Description Language HDL.
# The two major versions of HDL are Verilog and VHDL. At this point I am focusing on Verilog
# Goals
  - FSM Finite State Machine
  - UART Universal Asynchronous Receiver-Transmitter
  - SDRAM
  - ram & rom
  - fifo
  - SPI
  - Parallel data transfer
  - led digit display
  - oled displays
  - dsp
  - SOC
  - Simulation test bench
# Requirements
* GIT
* FPGA Field Programmable Gate Array Boards
    - Zedboard Xilinx Zynq 7000
    - XulA2-LX9 Xilinx Spartan 6 LX9
    - Arty Xilinx Artix-7 35T
    - Catboard Lattice ice40 HX8K
* Programming Languages
    - C
    - Python
    - Perl
    - Verilog

* Developement Hardware
    - Xilinx Ubuntu high development system
      - ISE
      - Vivado
    - RPi3B+
      - Software versions as 07/29/18
      - MyHDL a311468f
      - yosys e060375f
      - icestorm f0299751
      - arachne-pnr 5d830dd9
      - icozip 9dcbacfe
      - autofpga c0df9413
      - zipcpu ab82a886
      - verllator f0ed4346

.
# There are many tools that are required to write and simulate HDL.
* MyHDL Jan Decaluwe
    - Takes Python and creates Verilog or VHDL
    - MyHDL provides simulation & co-simulation with Icarus Verilog
* Simulators
    - Icarus Verilog Stephen Williams
      - Privides co-simulation with MyHDL
      - iverilog creates a module from verilog files
      - vvp
* Verilator Wilson Snyder
      - Converts Verilog to C
      - C simulation
* GTKWAVE Displays Value Change Dump VCD files generated with simulation
* Yosys Open Synthesis Suite Clifford Wolf
    - yosys
    - icestorm
- arachne-pnr
UART Universal Asynchronous Receiver-Transmitter
FSM Finite State Machine
Simulators

MyHDL Trace
“python trace_tx.py”
“gtkwave testbench.vcd”
The image below is the uart_tx simulation sending “helloworld”
A FSM is 'TX_IDLE', 'TX_START_BIT', 'TX_DATA_BITS', 'TX_STOP_BIT', 'TX_CLEANUP'
used in the design of the “uart_tx”.
A FSM is 'RX_IDLE', 'RX_START_BIT', 'RX_DATA_BITS','RX_STOP_BIT','RX_CLEANUP'

This is the echo of character with a Iverilog Simulation.
“python uart_rx.py” creates the Verilog uart_rx.v.
 “python uart_tx.py” creates the Verilog uart_tx.v.
“iverilog -o echo tb_dut_echo.v uart_rx.v uart_tx.v”
Creates the module “echo”
“vvp echo” executes the simulation creating “dump.vcd”
“gtkwave dump.vcd” is the command to view the VCD file.

START_BIT At 100 MHz 868 is the number of counts for 115200 Baud.
Note The uart_rx transistions from state 1 to state 2 earlier than the uart_tx.

Stop_BIT
Data